zmodem.doc !copyrighted by MCS 1994 use it anyway you like but don't complain
this file should be accompanied by a readme which contains some background
information on implementing zmodem.

GENERAL
-------

	Documentation about the zmodem protocol internals; should be sufficient
	to implement a completely functional zmodem protocol suite.
	
	Zmodem is a file transfer protocol that attempts to maximize bandwidth
	and minimize transfer times. it is a unidirectional protocol; i.e. the
	return channel only transfers control information; no data. either side
	may initiate the transfer; but the downloading site may respond to 
	an initialization frame by auto starting the download software.
	
	Schematically a zmodem file transfer in progress looks like this:

             |----------<< back channel <<-------------|
       ------+-------                          --------+------
       |   Sender   |                          |   Receiver  |
       |  (upload)  |                          |  (download) |
       --------------                          --------+------
             |---------->> data channel >>-------------|

	Multiple files may be transferred in one session.

SAMPLE
------

	all zmodem transactions are done using frames. a frame consists
	of a header followed by one or more data subpackets.
	a typical (simple) zmodem file transfer looks like this :

	    sender                      receiver

		ZRQINIT(0)
							        ZRINIT
		ZFILE
							        ZRPOS
		ZDATA data ...
		ZEOF
							        ZRINIT
		ZFIN
							        ZFIN
		OO

	zmodem continuously	transmits data unless the receiver interrupts
	the sender to request retransmission of garbled data.
	zmodem in effect uses the entire file as a window.


REQUIREMENTS
------------

	zmodem requires an 8 bit transfer medium; but allows encoded packets
	for less transparent media.
	zmodem escapes network control characters to allow operation with
	packet switched networks.

	To support full streaming, the transmission path should either assert
	flow control or pass full speed transmission without loss of data.
	Otherwise the zmodem sender must manage the window size.

	zmodem places no constraints on the content files.

LINK ESCAPE ENCODING
--------------------

	zmodem achieves data transparency by extending the 8 bit character set
	(256 codes) with escape sequences based on the zmodem data link escape
	character ZDLE

	Link Escape coding permits variable length data subpackets without the
	overhead of a separate byte count.  It allows the beginning of frames to
	be detected without special timing techniques, facilitating rapid error
	recovery.

	Link Escape coding does add some overhead.  The worst case, a file
	consisting entirely of escaped characters, would incur a 50% overhead.

	The ZDLE character is special. ZDLE represents a control
	sequence of some sort. If a ZDLE character appears in binary data,
	it is prefixed with ZDLE, then sent as ZDLEE

	5 consecutive CAN characters abort a zmodem session

	Since CAN is not used in normal terminal operations, interactive
	applications and communications programs can monitor the data flow for
	ZDLE.  The following characters can be scanned to detect the ZRQINIT
	header, the invitation to automatically download commands or files.

	Receipt of five successive CAN characters will abort a zmodem session.
	Eight CAN characters are sent (just to be on the safe side)

	The receiving program decodes any sequence of ZDLE followed by a byte with
	bit 6 set and bit 5 reset (upper case letter, either parity) to the
	equivalent control character by inverting bit 6.  This allows the
	transmitter to escape any control character that cannot be sent by the
	communications medium. In addition, the receiver recognizes escapes for
	0x7f and 0xff should these characters need to be escaped.

	zmodem software escapes ZDLE (0x18), 0x10, 0x90, 0x11, 0x91, 0x13,
	and 0x93. 
	If preceded by 0x40 or 0xc0 (@), 0x0d and 0x8d are also escaped to
	protect the Telenet command escape CR-@-CR. The receiver ignores
	0x11, 0x91, 0x13, and 0x93 characters in the data stream.


HEADERS
-------

	All zmodem frames begin with a header which may be sent in binary or HEX
	form. Either form of the header contains the same raw information:

	- A type byte

	- Four bytes of data indicating flags and/or numeric quantities depending
	  on the frame type

	the maximum header information length is 16 bytes
	the data subpackets following the header are maximum 1024 bytes long.

             M         L
      FTYPE  F3 F2 F1 F0   (flags frame)

             L         M
      FTYPE  P0 P1 P2 P3   (numeric frame)

    Beware of the catch; flags and numbers are indexed the other way around !

	16 BIT CRC BINARY HEADER
	------------------------
	
		A binary header is sent by the sending program to the receiving
		program. All bytes in a binary header are ZDLE encoded.
	
		A binary header begins with the sequence ZPAD, ZDLE, ZBIN.
	
		0 or more binary data subpackets with 16 bit CRC will follow depending
		on the frame type.
	
		* ZDLE A TYPE F3/P0 F2/P1 F1/P2 F0/P3 CRC-1 CRC-2
	
	
	32 BIT CRC BINARY HEADER
	------------------------
	
		A "32 bit CRC" Binary header is similar to a Binary Header, except the
		ZBIN (A) character is replaced by a ZBIN32 (C) character, and four
		characters of CRC are sent.
	
		0 or more binary data subpackets with 32 bit CRC will follow depending
		on the frame type.
	
		* ZDLE C TYPE F3/P0 F2/P1 F1/P2 F0/P3 CRC-1 CRC-2 CRC-3 CRC-4

	
	HEX HEADER
	----------
	
		The receiver sends responses in hex headers.  The sender also uses hex
		headers when they are not followed by binary data subpackets.
	
		Hex encoding protects the reverse channel from random control 
		characters. The hex header receiving routine ignores parity.
	
		use of hex headers by the receiving program allows control characters
		to be used to interrupt the sender when errors are detected.
		A HEX header may be used in place of a binary header
		wherever convenient.
		If a data packet follows a HEX header, it is protected with CRC-16.
	
		A hex header begins with the sequence ZPAD, ZPAD, ZDLE, ZHEX.  
		The extra ZPAD character allows the sending program to detect
		an asynchronous header (indicating an error condition) and then
		get the rest of the header with a non-error specific routine.
	
		The type byte, the four position/flag bytes, and the 16 bit CRC
		thereof are sent in hex using the character set 01234567890abcdef.
		Upper case hex digits are not allowed.
		Since this form of hex encoding detects many patterns of errors,
		especially missing characters, a hex header with 32 bit CRC has not
		been defined.
	
		A carriage return and line feed are sent with HEX headers.  The
		receive routine expects to see at least one of these characters, two
		if the first is CR.
	
		An XON character is appended to all HEX packets except ZACK and ZFIN.
		The XON releases the sender from spurious XOFF flow control characters
		generated by line noise. XON is not sent after ZACK headers to protect
		flow control in streaming situations. XON is not sent after a ZFIN
		header to allow proper session cleanup.
	
		0 or more data subpackets will follow depending on the frame type.
	
		* * ZDLE B TYPE F3/P0 F2/P1 F1/P2 F0/P3 CRC-1 CRC-2 CR LF XON
	
		(TYPE, F3...F0, CRC-1, and CRC-2 are each sent as two hex digits.)
	
	BINARY DATA SUBPACKETS
	----------------------
	
		Binary data subpackets immediately follow the associated binary header
		packet.  A binary data packet contains 0 to 1024 bytes of data.
		Recommended length values are 256 bytes below 2400 bps, 512 at 
		2400 bps, and 1024 above 4800 bps or when the data link is known to
		be relatively error free.
	
		No padding is used with binary data subpackets.  The data bytes are
		ZDLE encoded and transmitted.  A ZDLE and frameend are then sent,
		followed by two or four ZDLE encoded CRC bytes.  The CRC accumulates
		the data bytes and frameend.

	
PROTOCOL TRANSACTION OVERVIEW
-----------------------------	

	zmodem timing is receiver driven.  The
	transmitter should not time out at all, except to abort the program if no
	headers are received for an extended period of time, say one minute.
	
	SESSION STARTUP
	---------------

		To start a zmodem file transfer session, the sending program is called
		with the names of the desired file(s) and option(s).
	
		Then the sender may send a ZRQINIT header. The ZRQINIT header causes a
		previously started receive program to send its ZRINIT header without
		delay.
	
		In an interactive or conversational mode, the receiving application
		may monitor the data stream for ZDLE.  The following characters may be 
		scanned for B00 indicating a ZRQINIT header, a command to download
		data.
	
		The sending program awaits a command from the receiving program to
		start file transfers. 
	
		In case of garbled data, the sending program can repeat the invitation
		to receive a number of times until a session starts.
	
		When the zmodem receive program starts, it immediately sends a ZRINIT
		header to initiate zmodem file transfers, or a ZCHALLENGE header to
		verify the sending program.  The receive program resends its header at
		response time (default 10 second) intervals for a suitable period of
		time (40 seconds total) before exitting.
	
		If the receiving program receives a ZRQINIT header, it resends the
		ZRINIT header.  If the sending program receives the ZCHALLENGE header,
		it places the data in ZP0...ZP3 in an answering ZACK header.
	
		If the receiving program receives a ZRINIT header, it is an echo
		indicating that the sending program is not operational.
	
		Eventually the sending program correctly receives the ZRINIT header.
	
		The sender may then send an optional ZSINIT frame to define the
		receiving program's Attn sequence, or to specify complete control
		character escaping. if the receiver specifies the same or higher
		level of escaping the ZSINIT frame need not be sent unless an Attn
		sequence is needed.
	
		If the ZSINIT header specifies ESCCTL or ESC8, a HEX header is used,
		and the receiver activates the specified ESC modes before reading the
		following data subpacket.
	
		The receiver sends a ZACK header in response, containing 0.

	
	FILE TRANSMISSION
	-----------------

		The sender then sends a ZFILE header with zmodem Conversion,
		Management, and Transport options (see ZFILE header type) followed
		by a ZCRCW data subpacket containing the file name, file length and
		modification date.

		The receiver examines the file name, length, and date information
		provided by the sender in the context of the specified transfer
		options, the current state of its file system(s), and local security
		requirements.  The receiving program should insure the pathname and
		options are compatible with its operating environment and local
		security requirements.

		The receiver may respond with a ZSKIP header, which makes the sender
		proceed to the next file (if any) in the batch.

			The receiver has a file with the same name and length, may
			respond with a ZCRC header with a byte count, which
			requires the sender to perform a 32 bit CRC on the
			specified number of bytes in the file and transmit the
			complement of the CRC in an answering ZCRC header.the crc is
			initialised to 0xfffffff; a byte count of 0 implies the entire
			file the receiver uses this information to determine whether to
			accept the file or skip it.  This sequence may be triggered
			by the ZMCRC Management Option.

		A ZRPOS header from the receiver initiates transmission of the file
		data starting at the offset in the file specified in the ZRPOS header.
		Normally the receiver specifies the data transfer to begin begin at
		offset 0 in the file.

			The receiver may start the transfer further down in the
			file.  This allows a file transfer interrupted by a loss
			of carrier or system crash to be completed on the next
			connection without requiring the entire file to be
			retransmitted. If downloading a file from a timesharing
			system that becomes sluggish, the transfer can be
			interrupted and resumed later with no loss of data.

		The sender sends a ZDATA binary header (with file position) followed
		by one or more data subpackets.
	
		The receiver compares the file position in the ZDATA header with the
		number of characters successfully received to the file. If they do not
		agree, a ZRPOS error response is generated to force the sender to the
		right position within the file. (if the ZMSPARS option is used the
		receiver instead seeks to the position given in the ZDATA header)

		A data subpacket terminated by ZCRCG and CRC does not elicit a
		response unless an error is detected; more data subpacket(s) follow
		immediately.


		ZCRCQ data subpackets expect a ZACK response with the
		receiver's file offset if no error, otherwise a ZRPOS
		response with the last good file offset.  Another data
		subpacket continues immediately.  ZCRCQ subpackets are
		not used if the receiver does not indicate full duplex ability
		with the CANFDX bit.

		ZCRCW data subpackets expect a response before the next frame is sent.
		If the receiver does not indicate overlapped I/O capability with the
		CANOVIO bit, or sets a buffer size, the sender uses the ZCRCW to allow
		the receiver to write its buffer before sending more data.

			A zero length data frame may be used as an idle
			subpacket to prevent the receiver from timing out in
			case data is not immediately available to the sender.

		In the absence of fatal error, the sender eventually encounters end of
		file.  If the end of file is encountered within a frame, the frame is
		closed with a ZCRCE data subpacket which does not elicit a response
		except in case of error.

		The sender sends a ZEOF header with the file ending offset equal to
		the number of characters in the file.  The receiver compares this
		number with the number of characters received. If the receiver has
		received all of the file, it closes the file.  If the file close was
		satisfactory, the receiver responds with ZRINIT.  If the receiver has
		not received all the bytes of the file, the receiver ignores the ZEOF
		because a new ZDATA is coming. If the receiver cannot properly close
		the file, a ZFERR header is sent.

		After all files are processed, any further protocol
		errors should not prevent the sending program from
		returning with a success status.


	SESSION CLEANUP
	---------------

		The sender closes the session with a ZFIN header.  The receiver
		acknowledges this with its own ZFIN header.

		When the sender receives the acknowledging header, it sends two
		characters, "OO" (Over and Out) and exits.
		The receiver waits briefly for the "O" characters, then exits
		whether they were received or not.

	SESSION ABORT SEQUENCE
	----------------------

		If the receiver is receiving data in streaming mode, the Attn
		sequence is executed to interrupt data transmission before the Cancel
		sequence is sent.  The Cancel sequence consists of eight CAN
		characters and ten backspace characters.  zmodem only requires five
		Cancel characters, the other three are "insurance".

		The trailing backspace characters attempt to erase the effects of the
		CAN characters if they are received by a command interpreter.

	       char ses_abort_seq[] = {
				24,24,24,24,24,24,24,24,8,8,8,8,8,8,8,8,8,8,0
	       };


	ATTENTION SEQUENCE
	------------------

		The receiving program sends the Attn sequence whenever it detects an
		error and needs to interrupt the sending program.

		The default Attn string value is empty (no Attn sequence).  The
		receiving program resets Attn to the empty default before each
		transfer session.

		The sender specifies the Attn sequence in its optional ZSINIT frame.
		The Attn string is terminated with a null.


FRAME TYPES
-----------

	The numeric values are listed at the end of this file.
	Unused bits and unused bytes in the header (ZP0...ZP3) are set to 0.

	ZRQINIT
	-------

		Sent by the sending program, to trigger the receiving program to send
		its ZRINIT header.  
		The sending program may
		repeat the receive invitation (including ZRQINIT) if a response is
		not obtained at first.

		ZF0 contains ZCOMMAND if the program is attempting to send a command,
		0 otherwise.

	ZRINIT
	------

		Sent by the receiving program. ZF0 and ZF1 contain the  bitwise or
		of the receiver capability flags:

			CANCRY		receiver can decrypt
			CANFDX		receiver can send and receive true full duplex
			CANOVIO		receiver can receive data during disk I/O
			CANBRK		receiver can send a break signal
			CANCRY		receiver can decrypt
			CANLZW		receiver can uncompress
			CANFC32		receiver can use 32 bit Frame Check
			ESCCTL		receiver expects ctl chars to be escaped
			ESC8		receiver expects 8th bit to be escaped

		ZP0 and ZP1 contain the size of the receiver's buffer in bytes, or 0
		if nonstop I/O is allowed.

		while all these capabilities are nice in theory most zmodem implem-
		tations balk at anything other than 0,0. i.e. telix starts sending
		35 byte packets when CANFC32 is on.

	ZSINIT
	------

		The Sender sends flags followed by a binary data subpacket terminated
		with ZCRCW.

			TESCCTL		Transmitter expects ctl chars to be escaped
			TESC8		Transmitter expects 8th bit to be escaped

		The data subpacket contains the null terminated Attn sequence,
		maximum length 32 bytes including the terminating null.

	ZACK
	----

		Acknowledgment to a ZSINIT frame, ZCHALLENGE header, ZCRCQ or ZCRCW
		data subpacket.  ZP0 to ZP3 contain file offset.  The response to
		ZCHALLENGE contains the same 32 bit number received in the ZCHALLENGE
		header.


	ZFILE
	-----
		This frame denotes the beginning of a file transmission attempt.
		ZF0, ZF1, and ZF2 may contain options. A value of 0 in each of these
		bytes implies no special treatment.  Options specified to the
		receiver override options specified to the sender with the exception
		of ZCBIN.  A ZCBIN from the sender overrides any other Conversion
		Option given to the receiver except ZCRESUM.  A ZCBIN from the
		receiver overrides any other Conversion Option sent by the sender.


		ZF0: CONVERSION OPTION
		----------------------

			If the receiver does not recognize the Conversion Option, an
			application dependent default conversion may apply.

			ZCBIN "Binary" transfer - inhibit conversion unconditionally

			ZCNL Convert received end of line to local end of line
			     convention.  The supported end of line conventions are
			     CR/LF (most ASCII based operating systems except Unix
			     and Macintosh), and NL (Unix).  Either of these two end
			     of line conventions meet the permissible ASCII
			     definitions for Carriage Return and Line Feed/New Line.
			     Neither the ASCII code nor zmodem ZCNL encompass lines
			     separated only by carriage returns.  Other processing
			     appropriate to ASCII text files and the local operating
			     system may also be applied by the receiver. (filtering
			     RUBOUT NULL Ctrl-Z etc)

			ZCRECOV Recover/Resume interrupted file transfer.  ZCREVOV is
			     also useful for updating a remote copy of a file that
			     grows without resending of old data.  If the destination
			     file exists and is no longer than the source, append to
			     the destination file and start transfer at the offset
			     corresponding to the receiver's end of file.  This
			     option does not apply if the source file is shorter.
			     Files that have been converted (e.g., ZCNL) or subject
			     to a single ended Transport Option cannot have their
			     transfers recovered.


		ZF1: Management Option
		----------------------

			If the receiver does not recognize the Management Option, the
			file should be transferred normally.

			The ZMSKNOLOC bit instructs the receiver to bypass the
			current file if the receiver does not have a file with the
			same name.

			Five bits (defined by ZMMASK) define the following set of
			mutually exclusive management options.

				ZMNEWL Transfer file if destination file absent.  Otherwise,
				transfer file overwriting destination if the source file
				is newer or longer.

				ZMCRC Compare the source and destination files.  Transfer if
				file lengths or file polynomials differ.

				ZMAPND Append source file contents to the end of the existing
				destination file (if any).

				ZMCLOB Replace existing destination file (if any).

				ZMDIFF Transfer file if destination file absent.  Otherwise,
				transfer file overwriting destination if files have
				different lengths or dates.

				ZMPROT Protect destination file by transferring file only if
				the destination file is absent.

				ZMNEW Transfer file if destination file absent.  Otherwise,
				transfer file overwriting destination if the source file
				is newer.


		ZF2: TRANSPORT OPTION
		---------------------

			If the receiver does not implement the particular transport
			option, the file is copied without conversion for later
			processing. better not to use these; see readme

			ZTLZW Lempel-Ziv compression.  Transmitted data will be
			identical to that produced by compress 4.0 operating on
			a computer with VAX byte ordering, using 12 bit
			encoding.

			ZTCRYPT Encryption.  An initial null terminated string
			identifies the key.  Details to be determined.

			ZTRLE Run Length encoding, Details to be determined.

			A ZCRCW data subpacket follows with file name, file length,
			modification date, and other information described in a later
			chapter.

		ZF3: EXTENDED OPTIONS
		---------------------

			The Extended Options are bit encoded.

			ZTSPARS Special processing for sparse files, or sender managed
			selective retransmission. Each file segment is transmitted as
			a separate frame, where the frames are not necessarily
			contiguous.  The sender should end each segment with a ZCRCW
			data subpacket and process the expected ZACK to insure no data
			is lost.  ZTSPARS cannot be used with ZCNL.


	ZSKIP
	-----

		Sent by the receiver in response to ZFILE, makes the sender skip to
		the next file.

	ZNAK
	----

		Indicates last header was garbled.  (See also ZRPOS).

	ZABORT
	------

		Sent by receiver to terminate batch file transfers when requested by
		the user.  Sender responds with a ZFIN sequence. (or ZCOMPL in case of
		server mode).

	ZFIN
	----

		Sent by sending program to terminate a zmodem session. Receiver
		responds with its own ZFIN.

	ZRPOS
	-----

		Sent by receiver to force file transfer to resume at file offset
		given in ZP0...ZP3.

	ZDATA
	-----

		ZP0...ZP3 contain file offset. One or more data subpackets follow.

	ZEOF
	----

		Sender reports End of File.  ZP0...ZP3 contain the ending file
		offset.

	ZFERR
	-----

		Error in reading or writing file, protocol equivalent to ZABORT.

	ZCRC
	----

		Request (receiver) and response (sender) for file polynomial.
		ZP0...ZP3 contain file polynomial.


	ZCHALLENGE
	----------

		Request sender to echo a random number in ZP0...ZP3 in a ZACK frame.
		Sent by the receiving program to the sending program to verify that
		it is connected to an operating program, and was not activated by
		spurious data or a Trojan Horse message. this is the most simply 
		defeated security system ever invented. don't rely on it and better
		still don't use or implement it. build your security measures around
		starting the download at all and disallow explicit path names.

	ZCOMPL
	------

		Request now completed.

	ZCAN
	----

		This is a pseudo frame type in response to a
		Session Abort sequence.

	ZFREECNT
	--------

		Sending program requests a ZACK frame with ZP0...ZP3 containing the
		number of free bytes on the current file system.  A value of 0
		represents an indefinite amount of free space.


	ZCOMMAND
	--------

		ZCOMMAND is sent in a binary frame.  ZF0 contains 0 or ZCACK1 (see
		below).

		A ZCRCW data subpacket follows, with the ASCII text command string
		terminated with a NULL character.  If the command is intended to be
		executed by the operating system hosting the receiving program
		(e.g., "shell escape"), it must have "!" as the first character.
		Otherwise the command is meant to be executed by the application
		program which receives the command.

		If the receiver detects an illegal or badly formed command, the
		receiver immediately responds with a ZCOMPL header with an error
		code in ZP0...ZP3.

		If ZF0 contained ZCACK1, the receiver immediately responds with a
		ZCOMPL header with 0 status.

		Otherwise, the receiver responds with a ZCOMPL header when the
		operation is completed.  The exit status of the completed command is
		stored in ZP0...ZP3.  A 0 exit status implies nominal completion of
		the command.

		If the command causes a file to be transmitted, the command sender
		will see a ZRQINIT frame from the other computer attempting to send
		data.

		The sender examines ZF0 of the received ZRQINIT header to verify it
		is not an echo of its own ZRQINIT header.  It is illegal for the
		sending program to command the receiving program to send a command.

		If the receiver program does not implement command downloading, it
		may display the command to the standard error output, then return a
		ZCOMPL header.


	ZFILE FRAME FILE INFORMATION SUBPACKET
	--------------------------------------

		zmodem sends the same file information with the ZFILE frame data

		The pathname (file name) field is mandatory. each field after 
		pathname is optional and separated from the previous one by 
		a space. fields may not be skipped. the use of the optional
		fields is (by definition) optional to the receiver.

		PATHNAME
		--------

			The pathname (conventionally, the file name) is sent as a
			null terminated ASCII string. 
			No spaces are included in the pathname. 

			Filename Considerations

				- File names should be translated to lower case unless the
				  sending system supports upper/lower case file names. This
				  is a convenience for users of systems (such as Unix) which
				  store filenames in upper and lower case.

				- The receiver should accommodate file names in lower and
				  upper case.
	
				- When transmitting files between different operating
				  systems, file names must be acceptable to both the sender
				  and receiving operating systems.  If not, transformations
				  should be applied to make the file names acceptable. If
				  the transformations are unsuccessful, a new file name may
				  be invented be the receiving program.
	
				- If directories are included, they are delimited by /; i.e.,
	    		  "subdir/foo" is acceptable, "subdir\foo" is not.

	
		LENGTH
		------

			The length field is stored as a decimal string
			counting the number of data bytes in the file.

			The zmodem receiver uses the file length as an estimate only.
			It may be used to display an estimate of the transmission time,
			and may be compared with the amount of free disk space.  The
			actual length of the received file is determined by the data
			transfer. A file may grow after transmission commences, and
			all the data will be sent.

		MODIFICATION DATE
		-----------------

			The mod date is sent as an octal number giving the time the
			contents of the file were last changed measured in seconds from
			Jan 1 1970 Universal Coordinated Time (GMT).  A date of 0
			implies the modification date is unknown and should be left as
			the date the file is received.

			This standard format was chosen to eliminate ambiguities
			arising from transfers between different time zones.

		FILE MODE
		---------

			The file mode is stored as an octal string.
			Unless the file originated from a Unix system, the file mode is
			set to 0. 

		SERIAL NUMBER
		-------------

			set this field to 0.

		NUMBER OF FILES REMAINING
		-------------------------

			This field is coded as a decimal number, and includes the
			current file.  This field is an estimate, and incorrect values
			must not be allowed to cause loss of data.

		NUMBER OF BYTES REMAINING 
		-------------------------

			This field is coded as a decimal number, and includes the
			current file.  This field is an estimate, and incorrect values
			must not be allowed to cause loss of data. 

		FILE TYPE
		---------

			set this field to 0.

		The file information is terminated by a null.  If only the pathname
		is sent, the pathname is terminated with two nulls.  The length of
		the file information subpacket, including the trailing null, must
		not exceed 1024 bytes; a typical length is less than 64 bytes.


STREAMING TECHNIQUES / ERROR RECOVERY
-------------------------------------

	zmodem provides several data streaming methods
	selected according to the limitations of the sending environment,
	receiving environment, and transmission channel(s).
	
	WINDOW MANAGEMENT
	-----------------

		When sending data through a network, some nodes of the network store
		data while it is transferred to the receiver.  7000 bytes and more of
		transient storage have been observed.  Such a large amount of storage
		causes the transmitter to "get ahead" of the receiver. 
		This condition is not fatal but it does slow error recovery.
		
		To manage the window size, the sending program uses ZCRCQ data
		subpackets to trigger ZACK headers from the receiver.  The returning
		ZACK headers inform the sender of the receiver's progress.  When the
		window size (current transmitter file offset - last reported receiver
		file offset) exceeds a specified value, the sender waits for a
		ZACK packet with a receiver file offset that reduces the window
		size. ZRPOS and other error packets are handled normally.


	FULL STREAMING WITH SAMPLING
	----------------------------	

		If the receiver can overlap serial I/O with disk I/O, and if the
		sender can sample the reverse channel for the presence of data
		without having to wait, full streaming can be used with no Attn
		sequence required.  The sender begins data transmission with a ZDATA
		header and continuous ZCRCG data subpackets.  When the receiver
		detects an error, it executes the Attn sequence and then sends a
		ZRPOS header with the correct position within the file.
		
		At the end of each transmitted data subpacket, the sender checks for
		the presence of an error header from the receiver.  To do this, the
		sender samples the reverse data stream for the presence of either a
		ZPAD or CAN character (using rdchk() or a similar mechanism)
		. Flow control characters (if present) are acted upon.
		
		Other characters (indicating line noise) increment a counter which is
		reset whenever the sender waits for a header from the receiver.  If
		the counter overflows, the sender sends the next data subpacket as
		ZCRCW, and waits for a response.
		
		ZPAD indicates some sort of error header from the receiver.  A CAN
		suggests the user is attempting to "stop the bubble machine" by
		keyboarding CAN characters.  If one of these characters is seen, an
		empty ZCRCE data subpacket is sent.  Normally, the receiver will have
		sent an ZRPOS or other error header, which will force the sender to
		resume transmission at a different address, or take other action.  In
		the unlikely event the ZPAD or CAN character was spurious, the
		receiver will time out and send a ZRPOS header.
		The obvious choice of ZCRCW packet, which would trigger an ZACK from
		the receiver, is not used because multiple in transit frames could
		result if the channel has a long propagation delay.
		
		Then the receiver's response header is read and acted upon; starting
		with a resinchronize.
		
		A ZRPOS header resets the sender's file offset to the correct
		position.  If possible, the sender should purge its output buffers
		and/or networks of all unprocessed output data, to minimize the
		amount of unwanted data the receiver must discard before receiving
		data starting at the correct file offset.  The next transmitted data
		frame should be a ZCRCW frame followed by a wait to guarantee
		complete flushing of the network's memory.
	
		If the receiver gets a ZACK header with an address that disagrees
		with the sender address, it is ignored, and the sender waits for
		another header.  A ZFIN, ZABORT, or TIMEOUT terminates the session; a
		ZSKIP terminates the processing of this file.
		
		The reverse channel is then sampled for the presence of another
		header from the receiver (if sampling is possible). if one is detected
		another error header is read. Otherwise,
		transmission resumes at the (possibly reset) file offset with a ZDATA
		header followed by data subpackets.

	
	FULL STREAMING WITH REVERSE INTERRUPT
	-------------------------------------	

		The above method cannot be used if the reverse data stream cannot be
		sampled without entering an I/O wait.  An alternate method is to
		instruct the receiver to interrupt the sending program when an error
		is detected.
	
		The receiver can interrupt the sender with a control character, break
		signal, or combination thereof, as specified in the Attn sequence.
		After executing the Attn sequence, the receiver sends a hex ZRPOS
		header to force the sender to resend the lost data.
		
		When the sending program responds to this interrupt, it reads a HEX
		header (normally ZRPOS) from the receiver and takes the action
		described in the previous section. 
	
	FULL STREAMING WITH SLIDING WINDOW
	----------------------------------	

		If none of the above methods is applicable, hope is not yet lost.  If
		the sender can buffer responses from the receiver, the sender can use
		ZCRCQ data subpackets to get ACKs from the receiver without
		interrupting the transmission of data. After a sufficient number of
		ZCRCQ data subpackets have been sent, the sender can read one of the
		headers that should have arrived in its receive interrupt buffer.
	
		A problem with this method is the possibility of wasting an excessive
		amount of time responding to the receiver's error header.  It may be
		possible to program the receiver's Attn sequence to flush the
		sender's interrupt buffer before sending the ZRPOS header.


	SEGMENTED STREAMING
	-------------------

		If the receiver cannot overlap serial and disk I/O, it uses the
		ZRINIT frame to specify a buffer length which the sender will not
		overflow.  The sending program sends a ZCRCW data subpacket and waits
		for a ZACK header before sending the next segment of the file.

		A sufficiently large receiving buffer allows throughput to closely
		approach that of full streaming.  For example, 16kb segmented
		streaming adds about 3 per cent to full streaming zmodem file
		transfer times when the round trip delay is five seconds.


CONSTANTS
---------

	ASCII
	-----

		SOH			0x01
		STX			0x02
		EOT			0x04
		ENQ			0x05
		ACK			0x06
		LF			0x0a
		CR			0x0d
		XON			0x11
		XOFF		0x13
		NAK			0x15
		CAN			0x18

	ZMODEM	
	------

		ZPAD		0x2a	/* pad character; begins frames */
		ZDLE		0x18	/* ctrl-x zmodem escape */
		ZDLEE		0x58	/* escaped ZDLE */	

		ZBIN		0x41	/* binary frame indicator (CRC16) */
		ZHEX		0x42	/* hex frame indicator */
		ZBIN32		0x43	/* binary frame indicator (CRC32) */
		ZBINR32		0x44	/* run length encoded binary frame (CRC32) */

		ZVBIN		0x61	/* binary frame indicator (CRC16) */
		ZVHEX		0x62	/* hex frame indicator */
		ZVBIN32		0x63	/* binary frame indicator (CRC32) */
		ZVBINR32	0x64	/* run length encoded binary frame (CRC32) */

		ZRESC		0x7e	/* run length encoding flag / escape character */


	FRAME TYPES
	-----------

		ZRQINIT		0x00	/* request receive init (s->r) */
		ZRINIT		0x01	/* receive init (r->s) */
		ZSINIT		0x02	/* send init sequence (optional) (s->r) */
		ZACK		0x03	/* ack to ZRQINIT ZRINIT or ZSINIT (s<->r) */
		ZFILE		0x04	/* file name (s->r) */
		ZSKIP		0x05	/* skip this file (r->s) */
		ZNAK		0x06	/* last packet was corrupted (?) */
		ZABORT		0x07	/* abort batch transfers (?) */
		ZFIN		0x08	/* finish session (s<->r) */
		ZRPOS		0x09	/* resume data transmission here (r->s) */
		ZDATA		0x0a	/* data packet(s) follow (s->r) */
		ZEOF		0x0b	/* end of file reached (s->r) */
		ZFERR		0x0c	/* fatal read or write error detected (?) */
		ZCRC		0x0d	/* request for file CRC and response (?) */
		ZCHALLENGE	0x0e	/* security challenge (r->s) */
		ZCOMPL		0x0f	/* request is complete (?) */	
		ZCAN		0x10	/* pseudo frame; 
							   other end cancelled session with 5* CAN */
		ZFREECNT	0x11	/* request free bytes on file system (s->r) */
		ZCOMMAND	0x12	/* issue command (s->r) */
		ZSTDERR		0x13	/* output data to stderr (??) */

	ZDLE SEQUENCES
	--------------

		ZCRCE		0x68	/* CRC next, frame ends, header packet follows */
		ZCRCG		0x69	/* CRC next, frame continues nonstop */
		ZCRCQ		0x6a	/* CRC next, frame continuous, ZACK expected */
		ZCRCW		0x6b	/* CRC next, ZACK expected, end of frame */
		ZRUB0		0x6c	/* translate to rubout 0x7f */
		ZRUB1		0x6d	/* translate to rubout 0xff */

	RECEIVER CAPABILITY FLAGS
	-------------------------

		CANFDX		0x01	/* Rx can send and receive true full duplex */
		CANOVIO		0x02	/* Rx can receive data during disk I/O */
		CANBRK		0x04	/* Rx can send a break signal */
		CANCRY		0x08	/* Receiver can decrypt */
		CANLZW		0x10	/* Receiver can uncompress */
		CANFC32		0x20	/* Receiver can use 32 bit Frame Check */
		ESCCTL		0x40	/* Receiver expects ctl chars to be escaped
		ESC8		0x80	/* Receiver expects 8th bit to be escaped */